## Slide 1: Artificial neural networks as analysis tool for predicting EEG data in auditory attention tasks
Tobias de Taillez1
Bojana Mirkovic2
Birger Kollmeier1
Bernd T. Meyer1
University of Oldenburg, Germany, Department of Medical Physics and Cluster of Excellence Hearing4all
University of Oldenburg, Germany, Department of Psychology and Cluster of Excellence Hearing4all
Notes: Question that drives my PHD thesis:
Neural Networks are powerful. How could they be used for research?

## Slide 2
+45°
-45°
!
X
Alan J. Power et al. (2012): At what time is the cocktail party? A late locus of selective
attention to natural speech
Linear regression model
Edmund C. Lalor et al. (2009): Resolving Precise Temporal Processing Properties of the Auditory System Using Continuous Stimuli
Bojana Mirkovic et al. (2016): Target Speaker Detection with Concealed EEG Around the Ear
x(t)
ω(t)
y(t)

## Slide 3
Physical
Stimulus
Deep Neural Network Encoding Model
+45°
-45°
!
X
x(t)
y(t)
ω(t)
Physiological Data

## Slide 4: Deep Neural Networks
Powerful engineering tool
Work well in bad SNR situations
Can learn nearly any nonlinear transfer function
Powerful scientific tool also!
Contribution of input features can be calculated
This talk will show another way to learn from DNNs
S. Bach, A. Binder, G. Montavon, F. Klauschen, K.-R. Müller, W. Samek, On pixel-wise explanations for non-linear classifier decisions by layer-wise relevance propagation, PLOS ONE 10 (7) (2015) e0130140.
T. de Taillez et al. (2017): Machine learning for decoding listeners’ attention from electroencephalography evoked by continuous speech

## Slide 5: Deep Neural Networks
T. de Taillez et al. (2017): Machine learning for decoding listeners’ attention from electroencephalography evoked by continuous speech

## Slide 6
Experimental setup
16 participants
8 attended left speaker
50 min EEG and audio data per participant
84 channel EEG
Speech preprocessing
Envelope calculation
Envelope down-sampled to 64 Hz
z-scored over complete length
EEG preprocessing
Automatic bad channel detection with EEGLAB and reconstruction by interpolation
Down-sampled to 64 Hz
Highpass filtered at 1 Hz
z-scored over time in 1 min blocks
+45°
-45°
!
X

## Slide 7
Unattended
4 neurons
16 neurons
64 neurons
Attended
32 neurons
time context
Shifted across
Output matrix
84 neurons
channels
t0
Network Layout
2 input neurons
one attended channel
one unattended channel
3 hidden layer
4, 16 and 64 neurons
Output layer is a matrix
84 ∙ 32 =2688 neurons
for all EEG channels
500 ms time context
Shifted across

## Slide 8: Data split
Right story
Left story
Test set
Development set
EEG data
EEG data
EEG data
EEG data
EEG data
50 min
2 min
Cross-validation step
Data of all 16 participants is pooled
16 * 50 min = 800 min data
32 min excluded from training set
16 min development set
16 min test set
DNN training until no improvement on development set for 10 training epochs
25 cross-validation steps

## Slide 9: Sanity Check
Right story
Left story
EEG data
EEG data
EEG data
EEG data
EEG data
50 min
Cross-validation repeated
Misaligned stories
Same spectral properties of input features
DNN should not be able to learn any useful information from it!
Misalignment

## Slide 10: Model of Speech Processing
DNN is trained to model physiological speech processing
Model properties - calculating impulse response
Similar to ‚click‘ experiment
  click-length would be below 64 Hz resolution
0 0 0 0 0 0 0 1 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 1 0 0 0 0 0 0
Simulated auditory evoked potential
for unattended speech processing
Simulated auditory evoked potential
for attended speech processing
Picton, T. W., Hillyard, S. A., Krausz, H. I., & Galambos, R. (1974). Human auditory evoked potentials. I: Evaluation of components.

## Slide 12
Impulse Response
Cz excitation resembles auditory evoked potentials
  Even though trained on continuous speech!
Topological plot shows central activation
Attention effect
P2 peak is not present in unattended processing
Attention related activity at 200 ms and after 250 ms

## Slide 13: Spectral Aspects
EEG simulation of one input channel with complete story
Long term spectrum per channel
Averaging over channels
Complete story material
0 0 0 0 0 0 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 0 0 0 0 0
Complete story material
Long term spectrogram
- Unattended speech processing
Long term spectrogram - attended speech processing

## Slide 14
Difference
Spectral analysis
Comparable attended and unattended modeling
Difference between 4 and 6 Hz
Topologic view
Spectral power of each channel
Most power at 5 Hz is central
Attention related difference slightly lateral

## Slide 15: Summary
Spectral
Temporal
Spectral and temporal analysis come to similar results
Auditory attention effects are encoded between the N1 and P2
DNNs can provide a model for attention-related speech processing
DNNs are no “black box” approaches
Additional training data would improve models further
Higher frequency resolution possible!
P2

## Slide 16: Lookout
?
?
?
?
?
?

## Slide 17: Thank you for your auditory attention!
DNN code: